Specification of UCSC p-type detector (Ioffe):

SPb 7/11/2005

Footprint:		1.2 cm x 1.2 cm

Pitch: 			100 um

Implant width: 	10, 20, 40, 80 um

Metal width:	implant width + 4 um, metal has a window: length 2 mm  and metal bridge 7 um

Isolation:		Moderated p-spray 30 um ( alt. 30 um p-stop / 40 um poly?)

p-implants:		Atoll?

Biasing Resistors:	Polysilicon 1 M

Bias ring width:	50 um

Distance to ctr bias:	100 um

# of Guard rings: 	1

Guard ring width:	50 um

Distance to ctr bias:	100 um

Distance to edge:	700 um

Edge implant:		?

Number of strips:	64

Active width:		64*100 um = 0.64 cm

Width:			adjusted to the common cut line grid

Active Length:

Total length:

Pads			single row

Ctr bias line width:

Readout                       DC and AC coupling

# Text boxes

Bonding pads:

Bias ring:

Bias resistor: