PROPOSAL for a

# FIXTURE FOR BUILDING SILICON LADDERS

## SCIPP, 4/12/00

Motivations/ Requirements:

- Detectors vacuumed down during cure

- Bond line thickness controlled

- Reference pins for ladder edge straight to 10 microns

- Z controlled to avoid steps between detectors

- Microscope/CCD camera for QC

- Ergonomic, simple to use, stable, solid construction

Concept:

- One fixed block and 3 linear slides pinned on base plate

- All machining (XYZ) done after mounting slides on plate

- Delrin adapter plates mounted on all 4 pieces and vacuum chuck machined into surface.

- Pin holes bored in one machine setup (10 micron straightness)

- Stainless steel pins

- Lever action or eccentric pin used to move slides from zero position to 100 micron position. Each slide has one lever.

Procedure concept:

- All slides put in zero position by pushing levers one direction (clearly marked).

- First detector  placed on fixed block, pushed against pins, and vacuumed down

- Second detector dipped in glue, pushed against pins and previous detector, and vacuumed down

- Push lever to 2nd position to set 100 micron bond line

- Inspect bond line with CCD camera

- Repeat for third and fourth detectors

- Lower hood with UV lamps over top for curing

Estimated cost:

- 3 linear slides (ball bearing)		3 x $250		$750

- Materials						`		$500

- Machining					3 days			$2250

- Construction/QC				in house		$0

- Microscope, camera, monitor					$3000

- Microscope mount/ gantry					$1000

- Glue curing setup							???

### TOTAL								$7500 + curing setup

PROBABLE COST						< $10,000

Issues:

- What happens to the glue when you push the detectors together?

- Is UV light needed below the detectors?