DESIGN CONCEPT FOR GLAST TRAY PROTECTION

DURING ASSEMBLY AND STORAGE

# Gwelen Paliaga

May 5, 1999

SCIPP

Introduction:

We will attempt to design a protective cover (covers) for the GLAST trays which optomizes safety and ease of handling during all assembly steps.  These steps include; tray panel assembly, HDI mounting and wire bonding, detector placement and wire bonding, detector survey, and tower assembly.

Primary Issues:

- After full assembly there are only two available safe contact area with the tray.  These areas are the closeout sides perpendicular to the electronics.

- All the assembly steps require precision mechanical alignment which requires access to the tray corner posts both from the top and bottom and from the side.

- Wire bonding requires no protrusions above the Kapton plane higher than 0.060 in.

- Work holder weight limits on the wire bonder limit the tray cover pieces (not including the top cover which will be removed during bonding) to 3.5 lbs.

- Electrical testing and burning in of trays requires access for cables to reach the Nanonics connectors on both HDI’s

Design Concept:

Since the tray is assembled and testing in a linear fashion, the protective covers should be designed to be attached to the tray sequentially.  Ideally we would only place a protective cover on once, after one area of the tray is finished, and then never have to take it off.  This requires careful attention to interfacing with the various apparatus, jigs, fixtures, and tools used for testing and assembly.

For the prototype tower, tray assembly will happen in the following fashion:

- Build up tray panels with Kapton 				SLAC

- Glue assembled, wire bonded and tested HDI to Kapton		SCIPP

- Wire bond front-end chips to Kapton				SCIPP

- Bend HDI down and screw to closeout				SCIPP

- Align and glue detector ladders					SCIPP or SLAC

- Wire bond ladders to Kapton					SCIPP

- Electrical testing and burning in 					SCIPP

- Survey detector positioning					SLAC

- Tower assembly							SLAC

Tray assembly steps with addition of protective covers:

- Build up tray panels with Kapton				SLAC

- Attach rails with handles to the two free sides of the tray	SLAC

- Glue assembled, wire bonded and tested HDI to Kapton		SCIPP

- Wire bond front-end chips to Kapton				SCIPP

- Bend HDI down and screw to closeout				SCIPP

- Attach HDI cover end-caps					SCIPP

- Align and glue detector ladders					SCIPP or SLAC

- Attach cover top and bottom after ladder placement		SCIPP or SLAC

- Remove top or bottom to perform wire bonding			SCIPP

- Wire bond ladders to Kapton					SCIPP

- Electrical testing and burning in 					SCIPP

- Survey detector positioning					SLAC

- Tower assembly							SLAC

Tray assembly steps with protective covers and jigs or fixtures.

- Build up tray panels with Kapton					SLAC

- Attach rails with handles to the two free sides of the tray	SLAC

- Put tray on survey stage						SLAC

- Attach HDI alignment and gluing jig				SCIPP

- Glue assembled, wire bonded and tested HDI to Kapton		SCIPP

- Put tray in bonder work holder					SCIPP

- Wire bond front-end chips to Kapton				SCIPP

- Bend HDI down and screw to closeout				SCIPP

- Attach HDI cover end-caps					SCIPP

- Register SSD placement fixture					SCIPP or SLAC

- Align and glue detector ladders					SCIPP or SLAC

- Attach cover top and bottom after ladder placement		SCIPP or SLAC

- Remove top or bottom to perform wire bonding			SCIPP

- Put tray in bonder work holder					SCIPP

- Wire bond ladders to Kapton					SCIPP

- Plug in Kapton cables						SCIPP

- Electrical testing and burning in 					SCIPP

- Put tray on survey stage						SLAC

- Survey detector positioning					SLAC

- Tower assembly							SLAC

# THE PIECES

Rails:

- Made of 60-61 Al.

- Go on non-electronics sides.

- Don’t cover corner posts. Actually, are held back from the corner posts enough      (0.1 in.) to make room for the HDI alignment jig clamps.

- Protrude 0.060 in. beyond Kapton plane on both top and bottom.  This gives us the option of setting the tray down with no bottom cover.

- Have three small tapped holes on the top and bottom for attaching the cover sheets.

- Are cut away (2 in.) near corner posts to not protrude above the tray at all.

- Have small handles (Aluminum tabs) ~ 0.5 in. x 3 in. for carrying the tray and/or flipping it over.

- Have 3 tapped holes (4-40) to attach to the wire bonder.

HDI end-caps:

- Made of transparent material, or Al

- Can cover corner posts

- Screw into boss

- Don’t cover Nanonics connectors on each side of boss.

- Have a small lip on the side opposite the boss to protect the chip-Kapton bonds.

- Have 3 small screw holes for the cover sheet to attach to.  This is mostly to hold the end cap in place since it has nothing holding it on the side opposite the boss.

Cover Sheets:

- Made of composite perforated Al sheet and Mylar.  Or perforated acrylic with Mylar.  Depends on strength vs. weight requirements.

- Steps up around the edges to provide more clearance above detectors and bonds.

- Have cut-outs to access four the 4 corner posts and two Nanonics connectors (wide enough for Kapton cable

- Have clearance holes for screws to attach to 2 rails and 2 HDI end-caps.

- Have 2 pins for alignment and safety.  These should slip into holes in the two rails.

Summary:

There are three different pieces that make up the tray protection, Rails, HDI End-caps, and cover sheets.  Each tray needs 2 of each of these pieces.  For 18 trays we will then need 36 of each piece, or a total of 108 pieces.

Since this cover scheme does not completely enclose the tray we might want some other way to seal the completed trays for transport and storage.  This could be something as simple as a large zip-lock bag.