# Data Run Form

## Identification:

Principal Investigator:

Detector Serial Number: 		 (6127)

Experiment Type : 				 (Performance, Flux, Lifetime, etc.)

Date run started: 					 (YYMMDD)

Local PC Filename: 					 (6127PerformanceYYMMDD.txt)

Web e-Lab filename: 					 (6127.2008.0129.0)

## Objective:

## Geometry:

Date & Time of Geometry entry: 		       @

(mm/dd/yy @ hh:mm

## Settings:  (use V1 to display)

Channels enabled: 			 (all four, WC 00 1F)

Coincidence level: 			 (2-fold,   WC 00 1F)

Pre-Trig gate: 			 (40 ns, WT 01 00, WT 02 04)

Gate Width: 				 (100 ns, WC 02 0A, WC 03 00

PMT Voltage Settings:

Chnl 1				 ( 0.80 V)

Chnl 2				 ( 0.75 V)

Chnl 3				 ( 0.70 V)

Chnl 4				 ( 0.75 V)

## Run:

- Start Hyperterminal communications (115200 8N1 ANSI)

- Make sure computer has sufficient power, will not be tampered with and will not go into sleep or hibernate modes.

- Stop Scrolling of data	CD

- Start data capture to text file on PC

- Filename: 		 (6127Performance080129.txt)

- Reset Counters	RB

- Record Header info 	H1, V1, V2, DG, ST 2, DS, TI

- Start Scrolling of data:	CE

- Start Time: 		 (local time)

- At end of data run:

- Stop scrolling of data	CD

- Record Footer data	H1, V1, V2, DG, ST, DS, TI

- Stop data capture

- End Time: 						 (local time)

- Filesize: 			 (MB)

## Documentation:

- Be sure Geometry has been uploaded with a date/time prior to this data run:

  - Cosmic Ray e-Lab, Upload, Geometry

- Upload data file

  - Cosmic Ray e-Lab, Upload, Data

- Print Metadata page for file

- Run Analysis (performance, flux, shower, etc.) and print the graph and data.

- File all of these items along with this form in the Cosmic Lab binder.

## Remarks: