Dose – Contrast - Resolution Relationship

# Hartmut Sadrozinski 11/1/02

- Dose D = Energy Deposit/Volume	1 Gy ( =100Rad) = 1J/kg = 6.24 *1012 MeV/kg = 6.24 *109 MeV/g

- Define Voxel of Volume d3 and density 

Dose in Voxel DV = N*<E>/(*d3); N = # of protons, <E> mean energy loss

Total Dose = n*DV ; n = number of imaging settings in pCT = 20cm/d

- Mean Energy loss per proton  <E> =

- ,

for one 200 MeV proton, 1mm Voxel: Dv=4.53/0.01 MeV/g = 453*100/6.24 *109 [cGy] = 7.2*10-6  [cGy]

- Energy loss is measured with an ideal calorimeter with a resolution of 2%, including the natural spread due to energy straggling, or 4 silicon planes

or for 4 planes of silicon

- The mean energy <E> in a voxel is determined with a precision of

- Significance of signal SV in one Voxel of object O vs. background b:

- Assuming a needed significance of  SV = 3,



- Combining 4) and 8)   Energy per Voxel

- With 5)

,

Table 1: Number of Protons into a Voxel and the resulting Dose for two Resolutions

| E | DE/dx |  | N(0.5cm,0.1) | D(0.5cm,0.1) | 0.02*E | N(0.5cm,0.1) | D(0.5cm,0.1) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 100 | 7.29 | 9.2 | 0.161 |  |  |  |  |
| 150 | 5.45 | 16.7 | 2.7*106 | 0.95 | 3 | 8.7*104 | 0.03 |
| 200 | 4.53 | 23.5 | 7.8*106 | 2.3 | 4 | 2.3*105 | 0.065 |
| 250 | 3.95 | 33 | 2.0*107 | 5.1 | 5 | 4.6*105 | 0.12 |

1 for Al 5cm.

- With n = 20cm/d different settings, the total dose for n different measurements  with 3protons each in a voxel of side dimension d is

(see Fig. 1 for 200 MeV protons)

Fig 1. Total Dose for 2-dim pCT in a voxel of diameter d as a function of the density difference giving a 3 std signal. The proton energy is 200MeV, the number of settings is 20cm/d, and the number of protons is calculated for a 4 layer silicon detector and an “ideal” calorimeter with 2% energy resolution). With the present Si system, we can resolve 5mm voxels with 0.15 g/cm3 density difference at a dose of 1 cGy. With a 2% calorimeter, this number becomes 0.03cGy

References

[1] B. Keeney et al., “A Silicon Telescope for Applications in Nanodosimetry”, to be published in IEEE Trans. of  Nucl. Sciences .